## Slide 1: Smart Doorlock
Sokwhan Huh
Fall 16

## Slide 2: Smart Doorlock
0. Contents
Overview
Project Specifications / Requirements
Technology Background
Design (Hardware & Software)
Operation Modes
Demo
Cost Analysis
Results

## Slide 3: Smart Doorlock
1. Overview
Traditional door locks are…
Insecure & Inconvenient!
We need a better lock!

## Slide 4: Smart Doorlock
2. Project Requirements
Two ways to operate the door lock
  NFC (Smartphone Contact)
  IoT (Internet)
Grant / Revoke permissions
Manage access logs

## Slide 5: Smart Doorlock
3. Project Specifications
Supported Android versions (NFC): 4.4 (Kitkat) and above
NFC communication range: 5 cm max
Wi-Fi communication range: 50 meters max
AC power with DC battery backup
Minimum backup battery life of 24 hours

## Slide 6: Smart Doorlock
4. Technical Specifications
NFC
  ISO7816-4 / ISO14443a specification
  Android HCE (Host-card based emulation)
IoT
  MQTT Protocol
Software / Frameworks
  MCU: TI-RTOS, C language
  Server Side: NancyFX (WS), MySQL (DB), C# language
  Android App: Java

## Slide 7: Smart Doorlock
5. Technology (NFC)
NFC (Near Field Communication)
  A subset of RFID technology
  13.56 Mhz
  Close distance
  Applications range from commerce, bootstrapping connections, social networking etc.

## Slide 8: Smart Doorlock
5. Technology (NFC)
Protocol Stack
Source: https://commons.wikimedia.org/wiki/File:NFC_Protocol_Stack.png

## Slide 9: Smart Doorlock
5. Technology (NFC)
Protocol Stack & Flow (ISO 14443)
ISO/IEC 14443
ISO 14443-1 Physical Properties
ISO 14443-2 Type A
Power, Bit Transmission
ISO 14443-3 Type A
Activation, Anticollision
ISO 14443-4
Transport Protocol
ISO 7816-4 APDU, Application Protocol
NDEF (NFC Data Exchange Format)
Application Layer
Send REQA & SAK (Anticollision)
Respond ATQA & UID (Anticollision)
Send RATS & PPS (Transport)
Respond ATS & PPS (Transport)
Select AID (APDU)
Respond AID (APDU)
NDEF Comm. (Application)
Android Phone (HCE)
NFC Reader

## Slide 10: Smart Doorlock
5. Technology (NFC)
NDEF Structure
Source: https://www.safaribooksonline.com/library/view/beginning-nfc/9781449324094/ch04.html

## Slide 11: Smart Doorlock
6. Technology (IoT)
MQTT Protocol
  A lightweight protocol intended for Internet of Things
  Publish / Subscribe based
  On top of TCP / IP
Source: http://www.hivemq.com/blog/how-to-get-started-with-mqtt

## Slide 12: Smart Doorlock
7. Block Diagram

## Slide 13: Smart Doorlock
8. Design (Hardware, MCU)

## Slide 14: Smart Doorlock
8. Design (Hardware, TRF7970A)

## Slide 15: Smart Doorlock
9. Design (Software)
Initialize HW components (MCU, LCD, NFC Reader)
Create /Load Config File
IOT Enabled?
Connect to AP &
MQTT Broker
Start Menu Task
Start NFC Task
Start IOT Task
NFC
Enabled?
Y
N
Y

## Slide 16: Smart Doorlock
10. Operation Modes
Active
  Allows unlocking the doorlock by NFC / IOT
Configuration
  Register / Unregister phone
  Set doorlock mode (NFC only, IOT only, NFC & IOT)
  Wi-Fi Configuration

## Slide 17: Smart Doorlock
11. Operation – Doorlock Control
  To open the doorlock
    Tap a registered smartphone to NFC reader
    Use internet browser or Android Application

## Slide 18: Smart Doorlock
12. Configuration – Phone Registration
Enter registration mode in doorlock
Enter registration mode in Android application
Notes: https://www.youtube.com/watch?feature=player_detailpage&v=Cytk-GvEdA8#t=59

## Slide 19: Smart Doorlock
12. Configuration – Phone Registration
3) Tap phone to NFC reader
REG_PHONE|nu00rba1lhndk6ub36b78651f4
*Encrypted payload is sent
Notes: https://www.youtube.com/watch?feature=player_detailpage&v=Cytk-GvEdA8#t=59

## Slide 20: Smart Doorlock
12. Configuration – Wi-Fi
WIFI_CONFIG|SSID|TEST1AP|PASSWORD|PW123|SEC_TYPE|WPA2-PSK(AES)
*Encrypted payload is sent
Notes: https://www.youtube.com/watch?feature=player_detailpage&v=Cytk-GvEdA8#t=59

## Slide 21: Smart Doorlock
14. Demo Videos
NFC & IoT demo videos
Notes: https://www.youtube.com/watch?feature=player_detailpage&v=Cytk-GvEdA8#t=59

## Slide 22: Smart Doorlock
15. Cost Analysis
Type | Part name | Cost ($, USD)
Microcontroller Development Board (*) | Texas Instruments CC3200 Wireless MCU | 29.99
NFC transceiver Development Kit (*) | Texas Instruments TRF7970A booster pack | 24.99
Microcontroller | Texas Instruments CC3200 Wireless MCU | 12.16
NFC transceiver IC | Texas Instruments TRF7970A NFC / RFID Transceiver IC | 8.16
Keypad | Storm 720GFXI Series (7207-121W20) | 39.14
LCD | Newhaven Display Intl NHD-0420D3Z-NSW-BBW-V3 | 22.71
Power Supply | XP Power ECL30UD03-S AC/DC Converter | 66.00
Solenoid Motor | Adafruit 12V Lock-Style Solenoid | 14.95
Total (Excluding Development Parts, Denoted *) |  | 163.12
Total |  | 218.10

## Slide 23: Smart Doorlock
16. Results
Cost issues & PCB production limitation
  Development boards will be mounted to chassis
Notes: https://www.youtube.com/watch?feature=player_detailpage&v=Cytk-GvEdA8#t=59

## Slide 24: Smart Doorlock
16. Results
Both NFC & IoT operation works as intended
Requirements have been mostly met
  Battery backup system – cost & size issue
Notes: https://www.youtube.com/watch?feature=player_detailpage&v=Cytk-GvEdA8#t=59

## Slide 25: Smart Doorlock
Q & A?
Notes: https://www.youtube.com/watch?feature=player_detailpage&v=Cytk-GvEdA8#t=59